## Slide 1: Building a System for Energy measurement in OpenHardware
MiSCIT 2020-2021
  Supervisor: Jérôme FERRARI
  Co-Supervisors : Assoc. Prof. Benoit DELINCHANT
    Research Director Frédéric WURTZ
Student: HO Vu Duy Bao
Class: MiSCIT - IPA

## Slide 2: Plan
I. Introduction
Context
Objectives
II. System Analysis & Hardware
Linky & LinkyTIC
LoKy
III. LoRa & Application Server
LoRaWAN and TTN
Application server
IV. Review and Prospects
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects

## Slide 3
Smart building
Energy distribution:
Decentralization!!!
→ Complex set of producers and consumers
→ Difficult to manage
Solution?
28/06/2021
Introduction
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects

## Slide 4
Create a low-power device
Collect and secure data in a digital- safe using APIs
Data processing and visualization
The first step to build this system
Framework of project:
Collect and Process energy data at level of a city and internal of buildings
28/06/2021
Introduction
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
A system:
→ Manage the users’ energy consumption
→ Private communication network
Basic requirements

## Slide 5
28/06/2021
Solution
Figure 1: LoKy system blocks diagram
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Smart meter
Connection device
Datacenter
Application server

## Slide 6
28/06/2021
Linky
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Retrieve historical power consumption data
Control electrical appliances in customers' homes
Measure both of the electrical production and consumption
Receive bills based on the actual consumption
Figure 2: Linky smart meter

## Slide 7
28/06/2021
LinkyTIC
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Table 1: AlimTIC specification
Figure 3: Digital output TIC of Linky

## Slide 8: InfoTIC
28/06/2021
IINST : Instantaneous current in A,
PAPP : Apparent power in VA,
HCHC : Off-peak hours index in Wh,
HCHP : Full hours index in Wh,
BASE : Total consumption index in Wh
ASK signal with transmission rate 1200 bauds:
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects

## Slide 9
Figure 4: Arduino Pro Mini 3.3V (18x33mm)
Figure 5: RFM95W LoRa (16x16mm)
SPI
28/06/2021
µController & LoRa module
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects

## Slide 10: Low-Power Solution
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Figure 6: Power support module with Supercapacitor 0,47 Farad (@5.5V)
Figure 7: Optocoupler PC814
to Demodulate and Decode

## Slide 11: Combination
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Figure 8: LoKy support board (ver.0)

## Slide 12: Platform
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Figure 9: LoKy platform
Network Server
Forwarding LoRaWAN packets from LoKy to TTN
Linky TIC
LoRaWAN Gateway
TCP/UDP
Data transmission by LoRa
Database : InfluxDB
Visualizing : Grafana
(Grafana queries InfluxDB periodically via HTTPS)
HTTP/HTTPS
  LoKy
Collect Linky power consumption information
Self-powered by LinkyTIC
Arduino Pro Mini
3V3 8MHz
RFM95W
868MHz
SPI
UART
Application Server
Creating Internet connection for the applications
MQTT

## Slide 13: LoRa & The Things Network
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Open and free-to-use network server
*https://elainnovation.com/en/lorawan-private-network-vs-public-network-whats-the-difference/
Figure 10: LoRa in smart city

## Slide 14: LoRaWAN security
Figure 11: LoRaWAN security scheme
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
https://lora-alliance.org/wp-content/uploads/ 2020/11/lorawan_security_whitepaper.pdf
Notes: Network Session Key (NwkSKey): used by the network server to authenticate the device
Application Session Key (AppSKey): used by the application server to decrypt data from application server.

## Slide 15: TTN Mapper & LoRaWAN gateway coverage
Figure 12: LoRa coverage in Grenoble
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
18,3 Km

## Slide 16: The Trio: Node-RED, InfluxDB & Grafana
MQTT
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Figure 13: Data flow on the application server

## Slide 17: Prototypes
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Figure 14: LoKy debug board (ver.1)
Microcontroller
LoRa Module
Decoder
Power Support
Figure 15: LoKy device (ver.2)

## Slide 18: Prototypes
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Figure 16: LoKy integrated on Linky meter

## Slide 19: Results
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects
Figure 17: Data visualization on LoKy dashboard (Grafana)

## Slide 20: Review and Prospects
Points to improve:
A private network for LoKy
Users account management
System integration with the datacenter
Prospects:
Solved the decentralization in energy distribution
Created the stepping stone to develop for Smart City
28/06/2021
Introduction
System Analysing and Hardware
LoRa and Application server
Review and Prospects

## Slide 21
28/06/2021